## Slide 1: Plug-in Electric Vehicles
David Ellis
May 20, 2010
AABE National Conference

## Slide 2: In 1914, Detroit was the first American city to use electric taxi cabs
Detroit’s first electric taxi accumulated more than 46,000 miles in its first two years of operation.
Note the curb-side charging port and main charging stations.

## Slide 3: Electric drive technologies
Internal Combustion Engine (ICE)
Engine
Transmission
Differential
Engine
Transmission
Motor
Batteries
Differential
Mechanical Coupling
Hybrid Electric Vehicle (HEV)
Differential
Engine
Transmission
Mechanical Coupling
Batteries
Motor
Plug-in Hybrid Electric Vehicle (PHEV)
Engine
Motor
Batteries
Generator
Extended Range Electric Vehicle (EREV)
Motor
Batteries
Battery Electric Vehicle (BEV)
Plug-in Electric Vehicles (PEV)
Larger battery and less emissions
Today
Miles
Electric only: 10-20 ~40 100+

## Slide 4: Has technology gone to far?

## Slide 5: Electric drive technologies and annual electricity consumption
Chart: 
| ICE | HEV | PHEV 10 miles | EREV 40 miles | BEV 100+ miles
Annual Electric Sales/Vehicle (kWh) | 0 | 0 | 400 | 2000 | 2500
Column1 | 400 | 500
Annual Electricity Usage per Vehicle*
(kWh)
* Assumes a vehicle drives 12,500 miles / day, PHEV and EREV electric usage varies depending on drive characteristics, Chevy Volt-type vehicle at 5 mi/kWh
75% of Americans drive less than 40 miles on their daily commute
40 miles electric only - achieves similar GHG reduction as BEV - Limited need for public charging
BEVs will require faster charge rates and more daytime charging to address range “anxiety” - Needs public charging infrastructure

## Slide 6: In addition to technology advances, multiple factors are aligning to support a successful launch of PEVs
European Union target of 95 grams of CO2/km by 2020
=> 60 mpg
U.S.A.
Rest of World
China’s commitment to building 500,000/year hybrid and electric vehicles by 2012
Urban smog in emerging mega-cities
$2.4 Billion in U.S. stimulus dollars directed at advanced automotive batteries
Significant activity in Washington on federal climate legislation
Push for a domestic fuel source and fear of the return of high gas prices
Policy
Climate
Energy Security

## Slide 7: Plug-ins have a big fuel cost advantage …
* Gallon of gasoline equivalent price computed comparing ICE mileage of 26 mpg to PEV mileage of 5 mi/kWh at $0.10/kWh, 12,500 miles per year, undiscounted
Fuel Cost Comparison* ($/Mile)
$12,500 - $17,500 fuel savings over 10 years*
… but BIG upfront premium today
~$15,000 premium over regular car reduced by $7,500 tax credit
but for now, disadvantaged on purchase price
US example

## Slide 8: Electricity drive reduces GHG emissions and our addiction to imported oil
* 204 lb/MMBtu CO2 emissions rate (no carbon capture), 9,500 heat rate coal plant, 7,500 heat rate natural gas plant, ICE engine at 26 mpg, Hybrid drivetrain between 30-45 mpg, electric motor at 5 mi/kWh
Source: Argonne National Labs GREET Model, DTE Team Analysis
ICE
Hybrid
Coal
Natural Gas
Nuclear, Wind, Solar, etc.
Gasoline
Electricity (by source)
350
Future
Freedom from petroleum: electricity a domestic resource

## Slide 9: Infrastructure in place for broad PEV adoption
* PHEV is likely to also contribute to increased load during peak hours. Illustrative example of electric utility load – similar to Detroit Edison
** Estimated 600,000 cars and light trucks (does not include diesel trucks, buses, etc), 12,500 miles per year, 3.0 mi/kWh average efficiency, 75% electric operation
Source: DTE analyses, EPRI/NRDC Report
Impact of PEV on Typical Summer Load Profile (Ideal Case)*
ILLUSTRATIVE
MW
10% market share**

## Slide 10: Uncontrolled charging could lead to localized disruptions if not properly managed
Potential problems
  Voltage dips (dimming lights, damage to expensive electronics)
  Service interruption
  Transformer failure
Measures to address these issues
  On-vehicle charging control (time/date control)
  Utility notified at time of PEV purchase
  SmartGrid technology
Chart: kW
| 4.1666666999999998E-2 | 8.3333333000000023E-2 | 0.125 | 0.16666666699999988 | 0.20833333300000084 | 0.25 | 0.29166666700000243 | 0.33333333300000156 | 0.37500000000000139 | 0.41666666700000243 | 0.45833333300000001 | 0.5 | 0.54166666699999999 | 0.58333333299999957 | 0.62500000000000289 | 0.66666666700000277 | 0.70833333300000001 | 0.75000000000000289 | 0.79166666699999999 | 0.83333333300000001 | 0.87500000000000289 | 0.91666666699999999 | 0.95833333300000001 | 1 | 1.0416666669999932 | 1.0833333329999937 | 1.125 | 1.1666666669999999 | 1.2083333329999937 | 1.25
Weekday Load | 10.4 | 9.75 | 7.8 | 6.5 | 7.15 | 7.8 | 6.5 | 7.8 | 7.8 | 13 | 19.5 | 20.8 | 22.75 | 24.05 | 27.3 | 27.95 | 32.5 | 35.1 | 33.8 | 27.95 | 22.75 | 22.1 | 16.9 | 14.95 | 11.7 | 10.4 | 9.75 | 7.8 | 6.5 | 7.15
1.4 kW | 28 | 35.7 | 38.3 | 37 | 31.15 | 25.95 | 25.3 | 20.1 | 15
3.3 kW | 28 | 42.4 | 45 | 43.7 | 28
design | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
peak | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35
25 kVA Transformer with Uncontrolled PEV Load*
Summer Load 3 PEV @ 1.4 kW 3 PEV @ 3.3 kW
Peak Capacity
Design Capacity`
* 8-12 smaller, older homes per 25 kVA circuit. Most homes without central AC.
Load shape for warm summer day – adding 3 PEVs to a neighborhood

## Slide 11: DTE is working with Ford, GM and Chrysler on real-world testing
2009 Ford Escape plug-in hybrid electric vehicle
Testing is focused on:
  Battery technology
  Vehicle systems
  Customer usage
  Grid infrastructure
2011 Chevy Volt